## Slide 1
SINGLE-CHANNEL RF REMOTE CONTROL
One-Channel RF Remote
& Receiver Module
How it works · Where it works · How it can be used
433 MHz · ASK/OOK · Encoder–Decoder Pair

## Slide 2
INTRODUCTION
What Is a One-Channel RF Remote?
A single-channel RF (Radio Frequency) remote system is a two-part wireless switch: a handheld transmitter (TX) sends one ON/OFF command over radio waves to a receiver module (RX) that switches a single load — a light, motor, lock, or alarm.
"One channel" means the module controls exactly one output relay — a single press does a single job.
TX
Transmitter
RX
Receiver
Load switched: lamp, motor, lock, siren, buzzer…
02

## Slide 3
BUILDING BLOCKS
Key Components of the Module
1
RF Transmitter IC
Generates and modulates the 433 MHz carrier signal
2
RF Receiver IC
Tunes to 433 MHz and demodulates the incoming signal
3
Encoder IC
Converts the button press into a fixed digital code (e.g. HT12E)
4
Decoder IC
Validates the received code and activates the output (e.g. HT12D)
5
Antenna (TX & RX)
A short wire/helix that radiates and captures radio waves
6
Relay / Output Driver
Switches the connected load once a valid code is decoded
03

## Slide 4
CIRCUIT ARCHITECTURE · 1 OF 2
Transmitter (TX) Side
Battery
(3–12V)
Push
Button
Encoder IC
(e.g. HT12E)
RF TX
Module
Antenna
Pressing the button feeds a logic pulse to the encoder, which builds a fixed 12-bit address+data word. The RF transmitter IC uses this word to switch the 433 MHz carrier on and off, and the antenna radiates it as a radio wave.
04

## Slide 5
CIRCUIT ARCHITECTURE · 2 OF 2
Receiver (RX) Side
Antenna
RF RX
Module
Decoder IC
(e.g. HT12D)
Output
Driver
Relay
+ Load
The antenna picks up the radio wave; the RF receiver demodulates it back into a digital pulse train. The decoder checks the address bits and, only on a valid match, latches its data output — driving a transistor/relay that switches the load.
05

## Slide 6
WORKING PRINCIPLE
How It Works, Step by Step
1
Press
Button on the TX is pressed, closing the trigger pin
2
Encode
Encoder IC builds a fixed digital code word
3
Modulate
TX module keys the 433 MHz carrier (ASK/OOK)
4
Transmit
Antenna radiates the coded RF signal
5
Receive
RX antenna & module capture and demodulate it
6
Decode & Act
Decoder verifies the code and switches the relay
Total transmit-to-action latency is typically under 100 milliseconds.
06

## Slide 7
SECURITY LOGIC
Encoder–Decoder Address Matching
Chip pairs such as HT12E (encoder) / HT12D (decoder) split each transmission into an address and a data field. Both modules must share identical address-pin settings to "talk" to each other — this is what lets several remote/receiver pairs coexist without cross-triggering.
ENCODER (TX side)
• 8 address pins → set a unique ID
• 4 data pins → carry the button's bit
• Serial-out pin → feeds the TX module
• Same code re-sent while held down
DECODER (RX side)
• 8 address pins → must match encoder
• Compares incoming vs local address
• VT (valid transmission) pin flags a match
• Data pin output drives the relay/transistor
07

## Slide 8
AT A GLANCE
Typical Technical Specifications
433.92
MHz operating frequency
1
Output channel (relay)
≤100 m
Open-field range
3–12 V
Supply voltage (TX/RX)
ASK/OOK
Modulation scheme
<100 ms
Response latency
Exact figures vary by module grade, antenna design, and local RF regulations (e.g. FCC/ETSI limits).
08

## Slide 9
SIGNAL LAYER
Modulation: How the Code Rides the Carrier
Most low-cost modules use ASK/OOK (Amplitude Shift Keying / On-Off Keying): the carrier is simply switched on for a binary '1' and off for a '0'. This keeps the transmitter circuit extremely simple and cheap.
Data bits
1
0
1
1
0
0
1
0
RF carrier
Carrier ON = burst of RF energy (logic 1) Carrier OFF = silence (logic 0)
The decoder samples the carrier at the same bit rate and rebuilds the address+data word to compare against its own address.
09

## Slide 10
APPLICATIONS
Where a One-Channel RF Remote Works
1
Garage / gate automation
2
Home lighting on-off
3
Wireless door lock latch
4
Security siren / alarm trigger
5
Wireless doorbell
6
Industrial motor start-stop
7
RC toy / model single function
8
Car central-lock style switch
10

## Slide 11
GETTING STARTED
How to Set It Up and Use It
1
Wire the receiver
Connect RX module VCC/GND to supply, data-out to decoder, relay to the load.
2
Power the transmitter
Insert the battery (typically a 12V A23 or 3V coin cell) into the fob.
3
Match the address
Set the same address-pin pattern (or run the pairing routine) on TX and RX.
4
Mount the antenna
Keep TX and RX antennas straight and away from metal for best range.
5
Test the link
Press the button and confirm the relay clicks/LED lights within line of sight.
6
Install at final site
Fix the receiver near the load; carry the fob as the everyday remote.
11

## Slide 12
WHY USE RF
Advantages Over Wired or IR Control
✓
No line-of-sight needed
Works through walls, doors, and around corners — unlike infrared.
✓
Low component cost
A TX/RX pair typically costs less than a dollar in volume.
✓
Simple to integrate
Just a few pins: power, data, and an antenna wire.
✓
Low power draw
The transmitter draws current only while the button is pressed.
✓
Decent range
Tens to a hundred metres in open air, adjustable via antenna design.
✓
Multiple pairs coexist
Distinct addresses let several remote/receiver sets share a space.
12

## Slide 13
DESIGN CONSIDERATIONS
Limitations to Plan Around
!
Fixed-code cloning risk
Basic HT12E-style codes can be captured and replayed; use rolling-code ICs for security-critical locks.
!
Single output only
One channel = one action; multi-function control needs a multi-channel module.
!
Interference
Other 433 MHz devices, Wi-Fi harmonics, and metal enclosures can reduce range or cause misfires.
!
Regulatory limits
Transmit power and duty cycle must stay within local RF regulations (FCC/ETSI/WPC).
13

## Slide 14
SUMMARY
One Button, One Radio Link,
One Reliable Action
How: a button triggers an encoder, an RF pair carries the code, a decoder verifies it and fires a relay.
Where: garages, gates, lighting, locks, alarms, doorbells, and simple industrial or hobby switching.
How to use: match TX/RX addresses, mount antennas clear of metal, power up, and press to control.
Thank you
14