## Slide 1
AquaSense
Smart Water System with ESP8266 Wi-Fi and Android App Connection
No router • No mobile data • No Internet

## Slide 2
What Is AquaSense?
2
A smart water system built around an ESP8266 controller
Measures water level with an HC-SR04 and drives fill and drain pumps through an L293D module
Shows water percentage, pump status and history
Controlled from a phone over Wi-Fi: Fill, Drain and Stop
The ESP8266 creates its own Wi-Fi, so it works anywhere

## Slide 3
The Problem: Taking It Anywhere
3
AquaSense must work at school, a science expo, a friend's house, another building, or anywhere without mobile data or a home router.
Do not open Chrome every time
Do not type 192.168.4.1 every time
Do not configure a router at each place
Do not use mobile data
Avoid complicated Wi-Fi settings

## Slide 4
The Solution: ESP8266 as Access Point
4
The ESP8266 has Wi-Fi built in and acts like a mini router. The phone connects directly to it.
ESP8266
→
Wi-Fi: AquaSense
→
Phone
Wi-Fi name | Password | IP address
AquaSense | 12345678 | 192.168.4.1

## Slide 5
No Router, No Mobile Data, No Internet
5
The phone and ESP8266 form a local network, not an Internet connection
Works with mobile data OFF and no router
192.168.4.1 is a private address inside the ESP8266's own network
Chrome or the app asking for it is like saying: "ESP8266, give me the AquaSense page"
The phone may say "Connected without Internet": this is normal

## Slide 6
Why the IP Alone Is Not Enough
6
Phone connected to AquaSense Wi-Fi
Phone → ESP8266 at 192.168.4.1. Works.
Phone connected to home router
ESP8266 is not on that router, so the phone cannot reach it. Fails.
The app knowing the IP is not enough: a network path must exist. The ESP8266 supplies that path itself.

## Slide 7
Why an Android App?
7
Website way
Connect Wi-Fi → open Chrome → type 192.168.4.1 → wait → use website.
App way
Connect to AquaSense → open app → it connects to 192.168.4.1 → dashboard.
The app has a connection screen with an IP field
The IP can be remembered so it is typed once

## Slide 8
App Dashboard & Features
8
Water level percentage with animated tank
Pump status: ON / OFF
FILL, DRAIN and STOP buttons
Pump history and water-level history
Tank-height setting and instructions
Connection screen and status
Remember IP address
Automatic refresh
Error and reconnection handling

## Slide 9
Existing ESP8266 Endpoints Reused
9
Endpoint | Purpose
/data | Get water level
/fill | Start filling
/drain | Start draining
/stop | Stop pumps
/setHeight | Set tank height
/pumpHistory, /waterHistory | View history
/setTime | Set time
The app is another interface to the same controller, so the website is not thrown away.

## Slide 10
System Architecture
10
HC-SR04
Water level
ESP8266
Web / API + Wi-Fi AP
L293D → Fill Pump
Drain Pump
→
→
↓ Wi-Fi
Android phone → AquaSense app
Also: green LED = fill, orange LED = drain, optional local display.

## Slide 11
How to Operate
11
Power ON AquaSense; ESP8266 creates the "AquaSense" Wi-Fi
Connect the phone to AquaSense (password 12345678)
Open the AquaSense app; it uses 192.168.4.1
Dashboard appears with live water level
Fill, drain or stop the pumps; view history; change tank height

## Slide 12
Where & When It Can Be Used
12
Home
Monitor and control a water tank without a router.
School
Works without school Wi-Fi.
Science expo
Live demo on any phone within range.
Another building
Same steps at any location, unchanged.

## Slide 13
Limitations & Important Notes
13
The phone must be on the AquaSense Wi-Fi; typing the IP cannot create the connection
A phone normally joins one Wi-Fi at a time, so it has no Internet while connected
Range is limited to Wi-Fi range of the ESP8266
Fixed 192.168.4.1 is simple and reliable; aquasense.local may not work on every Android phone
Bluetooth was not chosen: Wi-Fi suits the dashboard, history and expansion

## Slide 14
Conclusion & Next Steps
AquaSense lets anyone control and monitor a water tank from a phone, anywhere, using only the Wi-Fi the ESP8266 creates itself: no router, mobile data or Internet.
Future: app that automatically finds the device, custom name instead of an IP, more app pages.
Thank you