## Slide 1
Arduino-Based Electronic Voting Machine
8 Candidates • NOTA • 50 Roll Numbers
Project presentation: prototype, working, uses and limitations

## Slide 2
What Is This Prototype?
2
An electronic voting machine built on an Arduino UNO R3
Uses a 16×2 I2C LCD, 4×4 membrane keypad, blue LED and buzzer
Designed to run a classroom election electronically
Handles up to 50 roll numbers, 8 candidates and NOTA
Records each vote, counts automatically and shows the winner
Everything is operated from a single keypad

## Slide 3
Objective & Main Features
3
Objective: accept selections, record and count votes, handle absent voters and NOTA, show results and identify the top candidate.
Roll numbers 1 to 50, one vote each
8 candidates plus NOTA
Absent voter skipping
Blue LED and buzzer confirmation
LCD instructions and results
Early end of voting
Candidate-wise, overall and winner display
No START button; normal power switch

## Slide 4
Components Required
4
Component | Quantity
Arduino UNO R3 | 1
16×2 I2C LCD | 1
4×4 Membrane Keypad | 1
Blue LED | 1
220 Ω Resistor | 1
Buzzer | 1
Jumper wires, breadboard, USB cable / power supply | As required

## Slide 5
Pin Connections & Block Diagram
5
Arduino Pin | Device
D2–D5 | Keypad R1–R4
D6–D9 | Keypad C1–C4
D10 | Blue LED via 220 Ω
D11 | Buzzer (+)
A4 / A5 | LCD SDA / SCL
5V / GND | LCD power; GND to LED, buzzer
4×4 Keypad (input)
↓
ARDUINO UNO
voting control • counting • results
↓
LCD
LED
Buzzer
LCD I2C address in code: 0x27

## Slide 6
Keypad Functions
6
Key | Function | Stage
1–8 | Select Candidate 1–8 | Voting
9 | Select NOTA | Voting
A | Skip absent voter | Voting
B | Submit selected vote | Voting
D | End voting immediately | Voting
# | Start election | Before voting
* | Open results screen | After voting
C | Candidate-wise results | Results
D | Overall result | Results
0 | Display winner | Results

## Slide 7
How It Operates: Start to Vote
7
1
Power ON
WELCOME / FOR VOTING
2
Press #
ELECTION STARTED
3
Roll No.
ROLL NO: 1 appears
4
Select
Keys 1–8, or 9 for NOTA
5
Press B
LED + beep, VOTE RECORDED
After about one second the machine moves to the next roll number. Repeat until the last voter.

## Slide 8
Special Situations
8
Absent voter
Press A. The roll number is skipped, no vote is counted, and the next roll appears.
NOTA
Press 9, then B. Counted in a separate NOTA counter.
B without choice
No vote recorded. LCD says SELECT CANDIDATE FIRST.
Early ending
Press D during voting to end at once. Roll 50 also ends voting automatically.

## Slide 9
Viewing Results
9
Voting ends: LCD shows VOTING COMPLETE
Press *: THANK YOU FOR VOTING, then results are unlocked
C: each candidate and NOTA shown in turn (about 2 s each)
D: overall totals in groups, since the LCD has 16 columns
0: winner with vote count, or TIE if top scores are equal
Only the selected counter rises per vote; skipped rolls add nothing

## Slide 10
Where It Can Be Used
10
Schools
Class monitor, house captain and student council elections.
Colleges
Class representative and club or society elections.
Exhibitions
Live demonstration of how electronic voting works.
Learning labs
Teaching Arduino, keypads, LCDs and vote counting logic.

## Slide 11
Real-Life Situations
11
Class election day
The teacher starts with #, calls roll numbers, and each student votes in turn.
Absentees
Press A for missing students so the election continues smoothly.
Time-limited voting
If the period ends early, press D and view results for votes so far.
Quick decisions
Small groups choosing a leader get instant results and a clear winner.

## Slide 12
How to Use It: Operator Guide
12
Connect the circuit and power the Arduino
Press # to begin; call each roll number in order
Voter picks 1–8 or 9 for NOTA; operator confirms with B
Press A only when the voter is absent
Press D during voting to stop early
After voting press *, then C, D and 0 for results
Do not switch off or reset before noting the results

## Slide 13
Advantages & Limitations
13
Advantages
Simple, low-cost, easy interface
No manual counting; instant results
Supports NOTA and absent voters
One keypad replaces many buttons
Limitations
Educational prototype, not for official elections
No authentication, encryption, audit or tamper resistance
Counts are in working memory; power-off or reset erases them

## Slide 14
Conclusion
This Arduino voting machine shows how a low-cost system can collect votes, count them automatically, handle absentees and NOTA, and declare a winner, making it ideal for classroom elections and demonstrations.
Thank you