## Slide 1
JAI GAME
ESP32 MPU6050 Motion-Controlled Gaming System
Tilt to play • Wireless • No internet needed

## Slide 2
What Is This Prototype?
2
A wireless game controlled by tilting an MPU6050 motion sensor
The ESP32 is both the controller and a Wi-Fi access point named "Jai Game"
The game is a web page hosted inside the ESP32
Phone, tablet or computer connects directly: no internet or mobile data
Two modes (Car Racing, Airplane) and three levels (Easy, Medium, Hard)

## Slide 3
Objectives
3
Build a motion-controlled game
Use ESP32 as the main controller
Create Wi-Fi directly from the ESP32
Host the game website on the ESP32
Control a game by movement, not buttons
Demonstrate accelerometer motion detection
Add multiple game modes and difficulties
Show real-time sensor processing
Combine hardware, wireless and web development

## Slide 4
Main Principle
4
Movement
→
MPU6050
→
ESP32
→
Command
→
Web Game
MPU6050 accelerometer senses the direction of tilt on X and Y axes
ESP32 classifies it as CENTER, RIGHT, LEFT, ACCELERATE or BRAKE
The browser asks the ESP32 for the command and moves the player

## Slide 5
Components & Software
5
Item | Purpose
ESP32 Development Board | Main controller, Wi-Fi, web server
MPU6050 module | Accelerometer and gyroscope
USB cable, jumper wires, breadboard | Power, programming, connections
Smartphone / computer | Displays the game
Arduino IDE (C/C++) | Programming the ESP32
Wire, Adafruit_MPU6050, Adafruit_Sensor, WiFi, WebServer | Libraries used

## Slide 6
ESP32 & MPU6050
6
ESP32
Reads sensor, processes motion, creates Wi-Fi, hosts the game. Built-in Wi-Fi, low cost.
MPU6050
3-axis accelerometer and gyroscope. Small, cheap, uses I2C. Tilt is read from accelerometer.
I2C link
Two lines only: SDA and SCL between ESP32 and sensor.

## Slide 7
Wiring & Wi-Fi Details
7
MPU6050 | ESP32
VCC | 3.3V
GND | GND
SDA | GPIO 21
SCL | GPIO 22
Wi-Fi setting | Value
Name | Jai Game
Password | 12345678
IP address | 192.168.4.1
Powered by USB; the sensor takes 3.3V from the ESP32.

## Slide 8
How Phone and ESP32 Talk
8
Browser
→
Request /motion
→
ESP32 reads MPU6050
→
Returns e.g. "RIGHT"
→
Game moves
HTML builds the menu and game area; CSS styles it
JavaScript runs game logic: obstacles, collisions, score, levels
The ESP32 web server serves "/" (game page) and "/motion" (command)

## Slide 9
Motion Control Mapping
9
Physical movement | Game action
Level / normal | CENTER
Back side lifted | RIGHT
Front side lifted | LEFT
Right side lifted | BRAKE
Left side lifted | ACCELERATE
Calibrated for this mounting orientation; thresholds on X and Y (about ±2.5 to ±3.0) may need retuning if the sensor is remounted.

## Slide 10
Game Modes & Difficulty
10
Car Racing
Multi-lane road; dodge oncoming cars; score rises for each obstacle avoided.
Airplane Mode
Fly an aircraft and avoid obstacles with the same controller.
Easy
Slower speed, more gap between obstacles.
Medium / Hard
Faster speed and more frequent obstacles; levels rise with score.

## Slide 11
How to Play
11
Power on the ESP32; it creates the "Jai Game" Wi-Fi
Connect the phone or computer (password 12345678)
Open a browser and enter 192.168.4.1
Choose Car Racing or Airplane, then Easy, Medium or Hard
Tilt the sensor to steer, accelerate and brake
Hit an obstacle and the game ends; restart from the menu

## Slide 12
Where It Can Be Used
12
Science and tech expos
Live interactive demo of sensors and wireless control.
Schools & labs
Learn embedded systems, I2C, Wi-Fi and web servers.
Interactive games
Motion-controlled play with no app needed.
Prototyping
Base for tilt-controlled interfaces and mini games.

## Slide 13
Advantages & Limitations
13
Advantages
Wireless; no internet or app needed
Fun motion-based control
Modes and difficulty levels
Low-cost, easy to demonstrate
Limitations
Mapping depends on sensor orientation
Sudden moves can give unstable readings
Limited Wi-Fi range; must stay connected
A demonstration, not a commercial platform

## Slide 14
Conclusion
JAI GAME turns physical movement into game commands, combining sensors, embedded programming, Wi-Fi networking and web development in one project. It can be expanded into more advanced games.
Thank you