## Slide 1
Smart Environmental Monitoring System
Using Arduino UNO, DHT11 and BMP280
Temperature • Humidity • Atmospheric Pressure

## Slide 2
What Is This Prototype?
2
An electronic system that monitors temperature, humidity and atmospheric pressure
Sensors collect the data; an Arduino UNO processes it
A 16×2 I2C LCD shows one reading at a time
The display changes automatically every two seconds
Simple, low-cost and useful for basic environmental monitoring

## Slide 3
Main Objectives
3
Measure surrounding temperature
Measure surrounding humidity
Measure atmospheric pressure
Process readings with an Arduino UNO
Display readings on an LCD
Change the display every two seconds
Learn practical use of sensors and microcontrollers

## Slide 4
Components Used
4
Component | Purpose
Arduino UNO | Main controller (ATmega328P)
DHT11 | Temperature and humidity
BMP280 | Atmospheric pressure
16×2 I2C LCD | Displays the readings
Breadboard | Circuit assembly
Jumper wires | Electrical connections
USB cable | Power and programming

## Slide 5
Sensors & Display
5
DHT11
Digital sensor for temperature and relative humidity. Data pin on D2.
BMP280
Digital sensor for pressure in hPa. Uses I2C.
16×2 I2C LCD
16 characters, 2 lines. I2C saves pins.
Both the LCD and BMP280 use I2C; they share A4 and A5 and have different addresses.

## Slide 6
Circuit Connections
6
DHT11 | Arduino
VCC | 5V
DATA | D2
GND | GND
BMP280 | Arduino
VCC | 3.3V
GND | GND
SDA | A4
SCL | A5
CS, SDO | Not connected
LCD | Arduino
VCC | 5V
GND | GND
SDA | A4
SCL | A5

## Slide 7
Block Diagram
7
DHT11
Temperature & Humidity
ARDUINO UNO
Process and control
→ digital
↓ I2C (A4, A5)
BMP280
Pressure sensor
16×2 I2C LCD
Display

## Slide 8
Basic Principle
8
1
Sensing
DHT11: temperature, humidity. BMP280: pressure.
2
Processing
Arduino UNO reads and processes the data.
3
Display
LCD shows each value for 2 seconds.
Sensing → Processing → Display

## Slide 9
How It Operates
9
Temperature
28.5°C
→ 2 s
Air Pressure
1012.4 hPa
→ 2 s
Humidity
62.0%
↺ 2 s
Switch on: Arduino starts the LCD, DHT11 and BMP280
Readings then repeat continuously in this order
No buttons or settings are needed

## Slide 10
Software & Libraries
10
Arduino IDE: write, compile, upload, and use the Serial Monitor
Language: C/C++ based Arduino code; setup() runs once, loop() repeats
DHT Sensor Library: for the DHT11
Adafruit Unified Sensor and Adafruit BMP280 libraries: for the BMP280
LiquidCrystal I2C Library: for the LCD
Output units: °C, %, hPa

## Slide 11
Where It Can Be Used
11
Homes
Indoor temperature and humidity.
Schools
Demonstrations and environmental studies.
Weather stations
Basic environmental readings.
Greenhouses
Watch growing conditions.
Laboratories
Conditions during experiments.
Offices
Indoor environment observation.

## Slide 12
Real-Life Situations
12
Comfort check
Is the room too hot or too humid? Read it at a glance.
Weather changes
Falling or rising pressure readings show changing conditions.
Plant care
Track greenhouse temperature and humidity.
Classroom demo
Show how sensors, Arduino and display work together.

## Slide 13
Advantages & Limitations
13
Advantages
Low-cost and easy to build
Real-time, automatic display
Common, easily available parts
Can add more sensors
Limitations
DHT11 is less accurate than advanced sensors
Readings stay local; not sent online
LCD shows limited information
For basic use, not professional weather work

## Slide 14
Conclusion & Future Improvements
The project shows how a microcontroller collects data from several sensors and presents it simply, a foundation for IoT weather stations and monitoring networks.
Future: ESP8266/ESP32 web dashboard, mobile app, SD card logging, graphs, buzzer alerts, light, air-quality or rain sensors.
Thank you